## Slide 1
University logo
Automated Robotic Surgery for Cyborg Locusts
Anton Salem1, Runkun Wang1, Shantanu Chakrabartty1,2
Washington University in St. Louis1, Adaptive Integrated Microsystems Laboratory2
gt
Introduction
Background
Project Goal
Methods
Results
Conclusions
Future Work
Acknowledgements
The authors thank Shantanu Chakrabartty, Barani Raman, and Jason Trobaugh for the opportunity to work in in the Adaptive Integrated Microsystems Laboratory and for their endless guidance throughout this project.
The motivation for this project comes from a team of engineers at Washington University in St. Louis in the Adaptive working to develop cyborg insects as bio-robotic sensing machines.
Odors prompt dynamic neural activity in the locust’s brain that allow the locust to correctly identify a particular odor in the presence of many.
It is advantageous to auto the surgical procedure to produce cyborg locus at scale.
Manipulator Hardware Development
Image Processing
The robotic manipulator was additively manufactured and fixed to a commercial XYZ linear stage.
The manipulator had five degrees of freedom, x, y, z, α, and 𝛿.
- XYZ Linear Stage (Left), Full Robotic Manipulator Render (Middle), and electrode inserter (Right).
Robotic Manipulator Design
-Continuous rotation servos (left) with feedback are coupled to the linear stage via additively manufactured adapters (right) and flexible drive shafts to control x, y, z, and α axis.
Closed Loop Control
-A simple PID controller is used to command the servo’s rotational angle (above) with the servo’s angular feedback signal.
Utilize electromechancial actuators, closed-loop control, and machine vision to design and develop a robotic manipulator that automates the process of electrode insertion at scale.
Robotic Manipulator Surgery
References
Locust with sensors placed to monitor neural activity1
[1] Saha, D., Leong, K., Katta, N. and Raman, B. (2013). Multi-unit Recording Methods to Characterize Neural Activity in the Locust (Schistocerca Americana) Olfactory Circuits.
[2] Savall, J., Tatt Wei Ho, E, Huang, C., Maxey, J., Schnitzer, M., (2015). Dexterous Robotic Manipulation of Alert Adult Drosophila for High-Content Experimentation.
[3] Chagas, M.A., Prieto Godino, L., Arrenberg, A., Baden, T., (2017) The 100 € lab: A 3-D printable open source platform for fluorescence microscopy, optogenetics and accurate temperature control during behaviour of zebrafish, Drosophila and C. elegans
[4] Barer, R., Saunders-Singer, A. E., A New Single-control Micromanipulator
Current approach: Electrode insertion is currently performed manually.
Locust in Mount
Manual Electrode Insertion
Olfactory lobes manually identified
Low cost, open loop, automated micro-manipulator.2
Approaches to perform automated surgery have been investigated.
Dexterous Manipulation of Fruit Flies.3
High-cost, commercially available automated micro-manipulator.4
An automated robotic manipulator is an effective method for the accurate surgical procedure of cyborg locusts.
The developed micromanipulator could be accurately controlled through a closed loop control system.
Image processing can be used to used to identify, characterize, and track the locust’s head.
Image Processing
Closed Loop Control System
Electromechanical Control
-A micro linear actuator controls the 𝛿 axis for electrode insertion (left).
Available solutions are expensive not significantly tailored to specific needs.
Initial Dynamic head tracking in MATLAB
  -Video feed sent to MATLAB (Left), image converted to black and white with head isolated (Middle), and real-time centroid tracking (Right).
Initial prototype surgery test proved promising for future developments.
The closed loop control system proved capable of accurately controlling the end effector on the micron level.
Feature and template matching techniques proved to be ineffective due to the high variability of size and pattern of the locust head.
Due to the variability in the size and patterns of a locust head, for accurate identification of areas of a locust head, machine learning techniques such as artificial neural networks should be explored.
More complex control algorithms can be explored to provide more robust and adaptive control to the manipulator.
-From left to right, a raw image of a locust head, another raw image of a locust head, harris features of the first locust head, feature matching between the two raw images, and black and white processed image of the first locust head with region of interest identified.